## Slide 1: Glaze3D
Petri Nordlund
Chief Architect
Bitboys Oy
(pnord@bitboys.fi)

## Slide 2: Introduction
Glaze3D is a new consumer-level 2D/3D-graphics accelerator chip
Fillrate: 1200 million texels / second
Designed and developed by Bitboys Oy, a Finnish 3D-graphics hardware company
Uses Infineon Technologies’ 0.20 m eDRAM process
9 MB of embedded framebuffer memory, 128 MB (max) of external video memory

## Slide 3: Design goals
Traditional, proven rendering architecture
PC’99, Microsoft Windows, Direct3D and OpenGL compatibility
Multi-chip support, two- and four-chip configurations
Support additional geometry processor, also in multi-chip configurations
Takes full advantage of embedded DRAM
Small and efficient rendering core required, embedded DRAM in Glaze3D takes most of the available silicon

## Slide 4: Performance
Quad-pixel pipeline @ 150 MHz
600 million pixels / second (dual textured)
1200 million texels / second
4.5 million fully featured triangles / second (sustained)
Cycle-accurate, bit-accurate simulator together with in-house developed PCIBuilder allows performance tuning with real-world applications (Quake III Arena, Viewperf)

## Slide 5: Performance
Texture cache: 16 KB cache for even mipmap levels and surface textures, 8 KB cache for odd mipmap levels and lightmaps. Both caches two-way set associative.
Block coverage issue - 4-pixel horizontal blocks, expect 90% coverage with average-size triangles
Quake III arena - 200 FPS with all features on @ 800x600x32
  400 MPIX/s
  350.000 drawn triangles/s
  3.5 MB of textures / frame, 670 MB/s of texture bandwidth
  Depth complexity of 4

## Slide 6: Features
4 simultaneous textures with trilinear filtering
DXTC texture compression
Full-scene, order independent anti-aliasing
Environment bump mapping
GDI+ features
Multiple scaled transparent video overlays
Digital flat-panel and TV-out support

## Slide 7: The Glaze3Dchip
304 pin BGA
1.5M logic gates
130 mm2 die size
External SDR SDRAM interface
  depth and/or color buffer stored here in higher resolutions
  max 128 MB
  64- or 128-bit interface
PCI and 2X/4X AGP interfaces: AGP interface supports direct AGP texturing

## Slide 8
Glaze3D architecture

## Slide 9: Triangle setup engine

## Slide 10: Pixel pipeline

## Slide 11: Why embedded DRAM?
Graphics accelerator needs GB/s of memory bandwidth, to render at 600 MPIX/s at true color and 32-bit Z, 7.2 GB/s of memory bandwidth is required
External memory can no longer provide enough bandwidth for future graphics accelerators
Cost-efficient - less chips on board
Reduced power consumption
Customized size - we needed exactly 9 MB (= 72 Mbits)
Customized organization in terms of bus width, banks, etc.

## Slide 12
Cell-concepts: Trench versus stack
Si surface
competitor’s HSG
block stacked cell
(hard to add multi-
level metallization)
Infineon’s trench capacitor cell
(ideally suited for adding multi-level metallization)
bitline with
BL contact
bitline
metal 1
trench
capacitor
Si surface
The trench technology combined with CMP (chemical mechanical polishing) techniques gives the advantage of being able to deposit the logic metallization onto a globally planar surface.

## Slide 13: Embedded DRAM
72 Mbits (9 MB) of eDRAM
150 MHz core/memory clock
9.6 GB/s memory bandwidth
512-bit interface
divided into four 18 Mbit modules of 3 banks each
Stores framebuffer and Z buffer - enough for 1024x768x32 bit
Wide internal buses, need lots of metal layers!

## Slide 14: Multichip configurations
Custom bus interface built into Glaze3D, a cost effective multi-chip solution
Thor is a geometry processor
The monster configuration is capable of 2400 MPIX/s, 10M triangles/s sustained - 4.8 gigatexels/s.
Target markets are:
  PC desktop high-end
  Arcade systems

## Slide 15: Tiled rendering order
Full linear framebuffer in video memory but primitives rendered as tiles instead of scanlines
Framebuffer is divided into tiles (16x16, 32x32, 64x64)
SLI is not sufficient - trashes texture caches!
In a four chip configuration, one chip renders 1/4th of the tiles
A Glaze3D-rendering chip ignores the primitive if it doesn’t fall into one of the tiles this chip renders
Framebuffer split between the rendering chips - monster configuration has a 36 MB embedded FB
Notes: Note: Traditional architecture, not like PowerVR or Talisman.
Maximum resolution in the monster configuration is 2048x1536 with true color and 32-bit IEEE floating point depth buffer!

## Slide 16
Technology
C9DD1
C10DD0
C10DD1
feature size
1Mb block size
raw gate density
45 Kgates/mm²
90 Kgates/mm²
0.20 µm
0.64 mm²
0.17 µm
0.38 mm²
0.15 µm
0.30 mm²
max. clock rate
200 MHz
250 MHz
~115 Kgates/mm²
300 MHz
bus width
512 bit
1024 bit
1024 bit
max. bandwidth
12 GByte/s
32 GByte/s
37 GByte/s
memory / logic on 150 mm²
100 Mbit 2.5 Mgates
140 Mbit 5 Mgates
180 Mbit 6.4 Mgates
Key parameters for next technologies

## Slide 17: Future
Pump more and more triangles through the pipeline
  Critical: CPU - 3D-hardware interface, drivers
  Geometry processors, advanced geometry processing
More pixels and texels
  Expect 8 gigatexels/s in 2001
  48 GB/s of memory bandwidth - embedded DRAM is the only solution!
More features per pixel
  better texture filtering (anisotropic for 2D only)
  programmability (procedural textures)
  realistic materials and surface properties

## Slide 18: Thank you!